## Slide 1: Introducing Nanode
An Open Source Network Applications Node
for the Internet of Things Hackathon April 8th/9th 2011
In Association with London Hackspace, Pachube & Arbour Wood Ltd.

## Slide 2: Nanode – In a Nutshell
Nanode – a low cost Network Applications Node
A Target to develop Web Connectivity Applications
Uses Pachube for Pub/Sub data & command exchange
“Nano-Tweet” M2M Messaging for Microcontrollers
A platform on which to build the Internet of Things
Versatile, open source firmware & hardware
Arduino compatible – so familiar to many developers
Under £20 (25 Euros, US$30) to make from a DIY kit
Nanode – Just Make It!

## Slide 3: Nanode – The Concept Emerges
First Prototype Breadboard August 2010
ATmega328
ENC28J60
74HC125
MagJack
FTDI cable
£10 in parts
Nanode – designed for low cost and easy to build

## Slide 4: Nanode - a simple DIY Kit

## Slide 5: Nanode - Empowered by
Pachube API using CSV data format
Publisher/Subscriber Model
Suits resource limited microcontrollers
Embeds both sensor data and serial commands into Pachube Feed
Simple serial protocol “Nano-Tweet”
M2M Messaging for Microcontrollers
5 second command latency is typical
Nanode - Connecting Environments

## Slide 6: Nano-Tweet - “Social Networking” for Microcontrollers
Nano–Tweet M2M Messaging for resource limited microcontrollers
Only need serial CSV string and simple Command Interpreter – Pachube does the rest
Alpha characters are Action Commands, Punctuation marks are control Primitives
Numbers are data Arguments Integers 0-65535 or decimals
Internet
RGB Lamp
Sensor Data, Trigger Event or Command String
A simple RGB Lamp Example
Publisher sends L,255,0,255 as CSV data string to a Pachube feed
Subscriber GETS L,255,0,255 from Pachube feed within 5 seconds
Decodes it to L (lamp) command and sets the R,G,& B LED PWM channels to 255,0,255 respectively – a nice warm mauve glow.
Publisher
Subscriber
Application

## Slide 7: Nanode - Uses familiar Arduino IDE
Atmel ATmega328 running at 16MHz
Microchip ENC28J60 Ethernet Controller
Pin Compatible with Arduino Shields
“Breadboard Friendly” I/O pins
Magjack, USB and FTDI interfaces
“Nano-bus” Local wired serial network
Wireless added as a low cost shield option
Programmed with Arduino IDE environment

## Slide 8: Nanode – can use Arduino shields

## Slide 9: Nanode built on low cost two layer PCB

## Slide 10: Nanode – Built for DIY Construction
Appeal to Enthusiasts, Colleges, Hackspaces
Through-hole conventional components
Uses DIL package, socketed ICs
All parts readily available
Only basic soldering and tools needed
Assembled in about 2 hours
Runs off 5V USB power or external 12V supply
Example Applications Code online
Very low cost kit < £20, 25 Euros, US$30

## Slide 11: Nanode is an Open Source Design

## Slide 12: Nanode uses Open Source Hardware
All Design files available on Thingiverse
Easy step by step instructions for DIY build
Schematic Diagram
PCB Board Files - popular Eagle CAD format
Applications Code Examples supplied
Bootloader uses Vusb Virtual USB & Metaboard
Hardware is closely compatible with Arduino
Nanode – Make it Happen

## Slide 13: Nanode - Applications
Smart Sensor Networks
Master/Slave Networks
Wired or Wireless
Wireless/Ethernet Bridge
Remote Control
Energy Monitoring
Home Automation
Internet of Things
Testing Putter/Getter with Pachube
RGB Lamp – We Love Nanode!

## Slide 14: Nanode – the Versatile Network Node
Internet
Application
Actuators
One Nanode Publisher
Sensors e.g. Temperature, Energy, Humidity, Radiation
Several Nanode Subscribers
Display
123.4
Nanode uses a Publisher/Subscriber Model

## Slide 15: Nano-Bus – A local Wired Serial Network
Internet
Sensors
Actuators
One Nanode Master
Several Nanode Serial Slaves on Nano-Bus
Display
123.4
Nano-Bus
Local Sensors & Applications
Nano-Bus extends the network capability >250m with wired serial Slaves. 4 wire cable carries application power & comms.

## Slide 16: Nanode as a Wireless Bridge
Internet
Sensors
Actuators
Wireless Shield
One Nanode Master
123.4
Nano-Bus
Nanodes fitted with wireless shields extend network to remotely located nodes – bridging them to the Internet
Wireless Shield
Wired Slaves
Wireless Slave
Remotely Located Display
Application

## Slide 17: Nanode – More Fun in Pairs!
Nanode - Just Make It!

## Slide 18: Nanode - Thanks
Code Design John Crouchley , Trystan Lea, Andrew Lindsay, Tuxgraphics
Hardware Design Ken Boak, Roger Light
Beta Testing Stephen Blomley, Samuel Carlisle, John Crouchley , Glyn Hudson, Trystan Lea, Andrew Lindsay
Original Idea Tuxgraphics 2007
In Association with London Hackspace Foundation, Pachube, OpenEnergyMonitor.org, Arbour Wood Ltd.
Nanode, designed for Hackspace
Empowered by
Nanode, an Arbour Wood design (c) 2011 ken.boak@gmail.com